## Slide 1: SolarWalk: Smart Home Occupant Identification using Unobtrusive Indoor Photovoltaic Harvesters
Nurani Saoda*, Md Fazlay Rabbi Masum Billah*, Victor Ariel Leal Sobral, Tushar Routh, Wenpeng Wang, Bradford Campbell
University of Virginia
ACM BuildSys’22, Nov 9-10, 2022
Link Lab

## Slide 2
Link Lab
Identifying occupants in smart homes is important
“Set the light to Relaxing evening”
“Start making cappucino”
“Play mozart”
“Set the thermostat to ‘Cozy winter’”
“Start dishwasher”
“Start deep cleaning”
“Get milk today”
“Left your keys”
{Event: “When Alice enters home” }
{Event: “When Alice exits” }
+ Improved user comfort and convenience + Reduce energy consumption

## Slide 3
Link Lab
Many smart building research has focused on this problem
Occupant Identification
Device-based
Camera/vision-based
Special purpose hardware-based (ultrasonic, acoustic)
RF-signal-based (Wifi, BLE)
Radar-based
On-device object-based

## Slide 4
Still, many practical challenges exist ..
Device-based
Camera/vision-based
Special purpose hardware-based (ultrasonic, acoustic)
RF-signal-based (Wifi, BLE)
Radar-based
On-device object-based
Requires user to wear/carry device
Privacy-invasive
Requires direct user interaction
Susceptive to signal multipath
Special purpose infrastructure required
Installation-heavy
Link Lab

## Slide 5
Link Lab
How can we design a smart home occupant identification system that -
Can be ubiquitously, unobtrusively, and scalably deployed
Builds on existing devices: Does not require additional hardware
Is installation-friendly
Is energy-efficient?
Notes: Build on existing systems
Does not require special-purpose hardware like Radar, sonar, acoustic Scalable
Installation-friendly: Does not require multiple devices

## Slide 6
We make several insightful observations
Link Lab
Movement and position sensor
Motion sensor
Electronic shelf labels
Door/window sensor
CO2 and Humidity sensor
Doorbell
Energy-harvesting sensors are replacing battery-powered device
Observation 1: PV cells are commonly used as a power source
Notes: Observations that are-> PV cells are very commonly used in energy-harvesting devices. Because of their availability and abundance The output can be a personal signature While PV cell has been used as harvesters- but not particulary as sensor

## Slide 7
PV Cell open circuit output voltage characteristics
Link Lab
Observation 2: Without external influence, output changes steadily, nearly constant in short period of time
Voltage
Current
VOC
ISC
I-V curve
Notes: Animation-> Person entering and leaving two different grahs

## Slide 8
Link Lab
PV cell output voltage fluctuates when a person passes by the sensor
Time
PV Cell voltage
Person A
Notes: Observations that are-> PV cells are very commonly used in energy-harvesting devices. Because of their availability and abundance The output can be a personal signature

## Slide 9
Link Lab
PV cell output voltage fluctuates when a person passes by the sensor
Observation 3: The voltage pattern is a unique signature of the person
Time
PV Cell voltage
Person B
Notes: Observations that are-> PV cells are very commonly used in energy-harvesting devices. Because of their availability and abundance The output can be a personal signature

## Slide 10
Link Lab
Voltage pattern changes with walking direction
Person A
Entry
Exit
Observation 4: The induced voltage pattern have a directional property
Notes: Observations that are-> PV cells are very commonly used in energy-harvesting devices. Because of their availability and abundance The output can be a personal signature

## Slide 11
SolarWalk identifies occupants in smart homes based on their unique voltage pattern on a PV cell and determines their movement direction.
Link Lab
We propose SolarWalk,
Notes: Observations that are-> PV cells are very commonly used in energy-harvesting devices. Because of their availability and abundance The output can be a personal signature

## Slide 12
Link Lab
SolarWalk Design: Event-triggered voltage sampling
Trigger generator
MCU+BLE
PV cell
SolarWalk Hardware
SolarWalk Classifier
Module
User device/IoT device controller
{Occupant id, Door event type}
[Voltage pattern]
trigger
sample
SolarWalk upgrades a PV cell to a person identifying sensor
Notes: When to start sampling voltage traces, how to sample for the voltage At what frequency

## Slide 13: Data collection and hardware prototype
Data collection platform
Hardware prototype
Solar cell
PIR sensor
nrF52840 board

## Slide 14
Data collection hardware
4 participants in 2 doors
1 participant in 1 door
Participants made 100 entry walks and 100 exit walks at each door
Each walk is 10 seconds long
Entry
Exit
Collecting voltage signatures for identification

## Slide 15: Example voltage trace from a single participant
Stopped walking
Started walking

## Slide 16
88% accuracy with 5 occupants
77% accuracy with 5 occupants
How accurate is SolarWalk?
Link Lab
Notes: Why is the event detection accuracy not 100% for one occupant?

## Slide 17
Does accuracy vary throughout the day?
Link Lab
Accuracy for identification and event detection does not vary significantly
Event detection
Identification

## Slide 18
Link Lab
How much deployment location matter?
Accuracy difference is within 3.9%
Accuracy drops at least 15% for Door 2

## Slide 19
Link Lab
Accuracy vs Occupant height
Maximum height results in maximum accuracy

## Slide 20
Link Lab
Concluding remarks
We present SolarWalk, an occupant identification system using small photovoltaic harvesters significantly improving deployability
SolarWalk demonstrates that a PV cell can be much more than a power source and converts it to a cheap, low-overhead sensor.
It is a stepping stone to enable more “harvester-enabled-sensing” applications.

## Slide 21: Thank you!
Link Lab
Questions?
Nurani Saoda
saoda@virginia.edu
I am on the job market for academia and industry!