## Slide 1: RetroIoT: Retrofitting Internet of Things Deployments by Hiding Data in Battery Readings
Nurani Saoda*, Victor Ariel Leal Sobral*, Ruchir Shah, Wenpeng Wang, Bradford Campbell University of Virginia
ACM MobiCom’22, Oct 17-21, 2022 Sydney, Australia
Link Lab

## Slide 2
Commercial IoT systems are not upgrade-friendly
End users can not add their own device
Upgrading or adding new functionality requires replacing all devices
Technology advances keep making devices obsolete
Link Lab
Let’s look at an example ..
What if the user wants a new trigger feature for the doorbell?
Press/motion activated blink video doorbell
Blink Gateway
Amazon cloud
Notes: Example: a door bell with a press switch upgrades to door bell if motion is detected
With closed source implementation we are simply limiting the potentials of existing facilities

## Slide 3
Users can not simply add a desired functionality to their device
Link Lab
Closed implementation of hardware and software impedes building on existing systems
Amazon cloud
Press/motion activated blink video doorbell
Blink Gateway
Notes: Example: a door bell with a press switch upgrades to door bell if motion is detected
With closed source implementation we are simply limiting the potentials of existing facilities

## Slide 4
Link Lab
What are the ways to add new features to an IoT system?
Software updates
Wait for the manufacturer to market version 2
Find a new device and completely re-build the whole network
Helps re-use some devices, but makes many current devices obsolete and contributes to e-waste.
Feature might not be available at all
Extremely time and cost-sensitive and maintenance-heavy
Hard to scale
Not enough without required hardware support
Get a new device from the same manufacturer
Availability
Does not benefit existing installations

## Slide 5
Instead .. Using existing infrastructure with minimal invasion can enable many retrofitting applications
Link Lab
Battery-powered devices can upgrade to energy-harvesting!
Users can add a new sensor with the device which the manufacturer does not provide
{
tamper_sensor: movement_detected: 0
_storage_condition:
{ temperature: 30 ℃
}
}
Important metadata can be attached
{
door_sensor:
_metadata:
{
category: “cabinet”
location: “living_room”
}
}
{
freezer_sensor: temp: 0℃
_expiration:
{ “Expires in 2 days!”
}
}
Product specific information can be advertised
Notes: Example: a door bell with a press switch upgrades to door bell if motion is detected
4344430993 432 box2
Energy-harvesting ttile should be different for the Data packet should be updated-> not this big devices

## Slide 6
But without completely new devices, how can we upgrade an IoT system with new functionality?
Observation 1: Many devices report battery readings with sensor data
Link Lab
Notes: Add snippets from sensor portal to show the battery voltage information The LoraWan-> not-so closed systems
BLE- closed systems. remove the 9 months

## Slide 7
But without completely new devices, how can we upgrade an IoT device with new functionality?
Link Lab
Observation 2: Batteries are easily accessible and user-servicable
Notes: Add snippets from sensor portal to show the battery voltage information The LoraWan-> not-so closed systems
BLE- closed systems.

## Slide 8
Link Lab
RetroIoT uses a device’s battery terminals to send additional data non-invasively and enables a new communication end point for IoT devices.
We propose RetroIoT,
Notes: In this paper, we present RetroIoT that encodes additional data into a device’s battery terminal non-vasively, making a new communication end point for an IoT device.

## Slide 9
Link Lab
Battery voltage data packets
Covert data
Data extracted in cloud
Modulated battery voltage
RetroIoT replaces a conventional battery with a programmable battery
COTS IoT Device
RetroIoT
New sensor
Metadata tag
programmable “smart” battery
Notes: RetroIoT replaces a traditional battery with a programmable battery that reads completely new data from external sensors and encode the information into the device’s battery port. The device unknowingly samples this new modulated battery voltage and transmits the battery voltage reading with its sensor data to the cloud application. The encoded data is retrieved at the cloud to infer the new sensor data. With this method, any device that samples and transmits battery voltage readings can encode additional data regardless of their communication protocols or device architecture.

## Slide 10
We must fulfill several requirements to design RetroIoT
Link Lab
Can not change device hardware and software
Operating voltage and current requirements must be met
The precision of the reported battery voltage reading limits data encoding bandwidth
New data must be encoded before the device samples battery voltage
Should be able to transmit data packet over multiple readings
Notes: RetroIoT must fulfill several design requirements to be successful:

## Slide 11
How does RetroIoT work?
Link Lab
IoT device
Analog input
Battery
Analog Encoder
Analog Encoder
Analog Buffer
Programmable LDO
Analog input voltage (V)
Encoded voltage at the battery terminal (V)
Encoder Transfer Function
Analog encoder receives analog voltage and converts to acceptable device operating voltage
RetroIoT analog encoder design:
Notes: Add animation Draw the circuit level diagram
for the enocder-decoder digital data-> encoded to the battery don't do that

## Slide 12
Link Lab
How does RetroIoT work?
Battery
Digital input
Digital Encoder
IoT device
Digital Encoder
Programmable LDO
DAC Current Source
MCU
RetroIoT digital encoder design:
Digital Symbols
Encoded voltage at the battery terminal (V)
Encoder Transfer Function
Digital encoder receives digital symbols and converts to acceptable device operating voltage

## Slide 13
Digital data encoding-decoding technique
Link Lab
With 12-bit ADC and 1mV decimal precision of reported battery voltage , we can encode 128 7-bit symbols between vmax = 3.3V, vmin = 3.0V.
vmin
vmax
vn = vn-1 + n*vrs
vmax = 3.3V
vmin = 3.0V
Encoding at RetroIoT
Decoding at Cloud
vmax
vmin
Notes: Add animation

## Slide 14
How to transmit more than 7-bit data packet? Multi-symbol metadata transmitting
The encoder needs to know when to encode the next symbol
Link Lab
Battery
IoT device
Digital Encoder
Programmable LDO
DAC Current Source
MCU
Digital input
Current monitor
Detects transmission current spikes
Needs to identify the start and end of the metadata
Long metadata format
vmin
vmax
vmin
vmax
Data 1
Data 2
Start
End
Notes: Add the BLE long metadata plot

## Slide 15
Link Lab
Mitigating the major source of battery voltage error
Linear interpolation using vmax and vmin :
= +
Here, v0 and v127 are reserved symbol for error calibration
ADC offset error contributes to the major source of error

## Slide 16
Interestingly, we can just completely replace the battery with a energy-harvesting power supply
But energy is limited now, how to adapt to changes in the available energy?
Link Lab
Energy-harvesting power supply running DPM
Battery voltage [sampling rate]
Control message [sampling rate]
Digital Encoder
Decoding in Cloud
IoT device
Battery
Sensor data [battery voltage]
Notes: Add animation

## Slide 17
How did we implement RetroIoT?
Analog Encoder
Digital Encoder
Energy-harvesting power supply board
Link Lab
Notes: Might be optional, not too detailed

## Slide 18
Link Lab
We demonstrate several retrofit applications using COTS devices
Door sensor with location tag
Gateway
Sensor payload
LoRaWAN packet
Soil moisture sensor
Header
Soil moisture and temperature readings
Battery voltage
5 Bytes
32 Bytes
2 Bytes
Example: 0x0b3b -> 2875 mV
One BLE sensor temperature and humidity sensor
Two commercial LoRa sensing device
Door sensor
Soil moisture sensor
Notes: sensor emperature-> source the images->

## Slide 19
Digital symbol transmission using digital encoder
Channel + Encoder Error
Temperature sensing using the analog encoder
Channel + Encoder Error
What is the end-to-end battery voltage error?
Link Lab
20.91 mV
3.96 mV
Notes: Might be optional, not too detailed temparature error->
error can be minimized at the cost of device complexity channel? the actual voltage-> What is the channel error? explain more remove-> channel with channel+encoder CDF- interpolation Battery voltage is sacrifice-> 6

## Slide 20
Does ADC resolution of the IoT device matter?
Link Lab
Channel + Encoder Error
2x reduction in error
Notes: Might be optional, not too detailed

## Slide 21
Link Lab
Metadata example
Demo app: upgrading a door sensor with installation-specific metadata
Format of the digital symbol
COTS Door Sensor
Battery
RetroIoT Digital Encoder
Notes: metadata illustration
could be shown in the motivation
outline or the section-> its getting lost in the slides Do not rush add the retrofit channels at the end

## Slide 22
Link Lab
Demo App: upgrading a door sensor with installation-specific metadata
Successfully decoded all 12 metadata
Channel + Encoder Error
Notes: metadata illustration
could be shown in the motivation
outline or the section-> its getting lost in the slides Do not rush add the retrofit channels at the end

## Slide 23
Link Lab
What other data open channels exist beside battery voltage?
Awair Glow devices have a switchable outlet where binary data can be encoded
Smart key pads can log any arbitrary pin beyond the actual lock code
Smart sprinkler controllers allow connection for external sensors like rain sensor
Notes: metadata illustration
could be shown in the motivation
outline or the section-> its getting lost in the slides Do not rush add the retrofit channels at the end

## Slide 24
Concluding remarks
RetroIoT demonstrates how existing devices can upgrade them just by replacing their battery
Demonstrates a minimally invasive technique to transmit additional data
RetroIoT will enable further research to leverage new open data channels

## Slide 25: Thank you!
Link Lab
Questions?
Nurani Saoda
saoda@virginia.edu